## Slide 1: Cache Partitioning A Solution for Cache Pollution
Ammar Saeed

## Slide 2: Contents
Cache Pollution
Partitioned Cache Design
Benchmark Results
Use Case Scenarios
Conclusion

## Slide 3: Cache Pollution In Multicore Architectures
A Generic Multicore Architecture
  Individual L1 data and instruction caches
  Shared L2 Caches
  Shared L3 Cache
Cache Pollution
  Unnecessary data caching
  Resulting in eviction of useful data
Cache Pollution from different Cores
Effect of Inclusive caches on Cache Pollution

## Slide 4: Cachebench Benchmarking
Cachebench : Linux LLC benchmark for cache performance.
Replacement of BW with miss rate using ARM PMU
Scenarios:
  No process running on other core (No Load)
  A heavy cache pollution process on other core (Load)
  Different test times

## Slide 5: Effect of Cache Pollution (1)
Increase in miss rate from less then 1 % to up to 20 %
Effect is time dependent
Effect of L1 Size and L2 Size
  As vector size exceed L1 size the hit rate increase, that’s why effect not visible in range from 32K
  As vector size increase L2 size, most access creates misses that’s why cache pollution is not visible

## Slide 6: Effect of Cache Pollution (2)
Increase in miss rate from less then 1 % to up to 20 %
Effect is time dependent
Effect of L1 Size and L2 Size
  As vector size increase L1 size the hit rate increase, that’s why effect not visible in range from 32
  As vector size increase L2 size, most access creates misses that’s why cache pollution is not visible

## Slide 7: Cache Partitioning Prototype
Idea : Avoid cache pollution from different cores
Basic Principle:
  Each core assigned with some partition of cache
  Core only cache data within its partition
  Partitions can overlap
Prototyping Platform (Juno Board):
  Dual Core Cortex A57
  Quad Core Cortex A53
  FPGA Board Attachment (LogicTile FPGA Board)

## Slide 8: Design
Partition allocation through mask bits for each way per core
Only masked ways can be replaced
Partitioning of Cache in Vertical blocks
Different masking for each block
Benchmarking (Cachebench)
  Mapping of vector to partitioned cached
  Vector uncached in local SoC caches
  Replacement of ARM PMU with Partitioned Cache monitors
Line Size | 64 byte
Associativity | 8 Way
Write Policy | Write back
Cache lines | 1024
Blocks | 4 Blocks (256 Lines x 8 way each)
Partition configuration granularity | 256 Lines x 16 way (One block)
Cached Memory | 128 MB
Cached Address | 0x68000000 - 0x6FFFFFFF
Configuration Memory | 16 Word (64 bit wide)
Configuration Memory Base Address | 0x61000000

## Slide 9: Benchmark with Partitioned Cache – Read
Miss rate close to no load achieved
Increase in miss rate as vector size goes out of assigned partitions

## Slide 10: Benchmark with Partitioned Cache – Read Write
Miss rate close to no load achieved
Increase in miss rate as vector size goes out of assigned partitions

## Slide 11: Use Cases
Heterogeneous Platforms
  Cache pollution from different type of processing platforms (LL Shared cache between DSPs CPU GPUs etc)
  Dynamically allocating partitions to each processing unit as per requirement
Datacenters
  Cache pollution effects between different VMs
  Solution: Having cache partitioning for different VM

## Slide 12: Use Cases (2)
Real Time Systems
  Cache pollution can effect the deterministic behavior of an application
  Many real time systems have hard or soft real time requirements for different applications
  Base Transceiver Station
  Automotive Controllers
  Today’s Real Time Controllers = Manycore !
  Solution : Tie up time critical application to particular cores with allocation required partition sizes

## Slide 13: Conclusion
Cache pollution can effect miss rate (increase from ~1% to ~20%)
Partitioning can mitigate the cache pollution effect
Cache partitioning can be useful in application ranging from embedded to data centre applications