## Slide 1: Internship Prsentation 1
Uzair Sharif

## Slide 2: Outline
Virtual Platforms, OVP
Initial Issues
Monitoring System Performance
Current Status

## Slide 3: Virtual Platforms
Captures the entire HW in an executable program that we can debug by running the same SW on it that will eventually be run on actual HW
  Common use-cases for VPs are SW development/verification, HW/SW performance verification, Early architecture exploration and HW/SW functional verifiaction
Many VP solutions like proprietary VPs being provided by Synopsys, Cadence etc as well as Open Source like OVP, QEMU, GEM5 etc – we decided to go with OVP
OVP
  Open Source, Customizable – can build entire platforms of your own using component models
  Full system platforms based on programmer’s view (LT) models primarily intended for SW development targeting those platforms
  Huge variety of virtualized versions of real platforms available to run:
    ARM, MIPS, PowerPC, Xilinx based platforms and many other
    Unicore, multicore CPU models
    Baremetal/ Linux OS/ RTOS support
    SystemC-TLM2.0 interface available
  Specifically for ARM, useful platforms available for use:
    Minimal ArmCortexA9-MPx4 based system (running uKernel)
    ARM-Integrator-CP board (ARM926EJS/ ARMCortexA9-UP, Linux/Nucleus/eCos)
    ARM-Versatile-Express board (ARMCortexA9_MP/ARMCortexA15-MP, Multiple ARM CMPs, Linux SMP)
    ARM Cortex-A57MP based (ARMv8-A, Linux SMP) – but needs full product license to run!!

## Slide 4: ARM-Versatile-Express VP (SystemC)
ARM_CortexA9_MP
System Bus
(Rest of the Platform)
SystemC Top

## Slide 5: Initial Issues (1)
Problem: Only one instruction/data port interface for the whole CPU model, so no way to know which smp core initiated the memory transaction
Solution:
  Modified the OVP CPU model’s internal port class to have instruction/data port pair for each of the smp core
  Using the ICM-API provided by OVP, we find the ICounts for each of the smp core and comparing with past ICounts, we find the smp core that initially requested the transaction – then we simply forward the request to its specific port
    This won’t work for data accesses as for them ICounts remain the same – here we assume that data accesses will always correspond to previous instruction requests as OVP models are instruction accurate so we using the smp core earlier in instruction fetch we forward these data access transactions on the same smp’s data port

## Slide 6: Initial Issues (2)
Problem: While running simple memory read/write Linux application on all smp cores, we came to know that OVP model executes instructions for each smp core in batch controlled by quantum size. The default quantum size is too big to see any simultaneous memory accesses even though all apps are running concurrently on linux-smp kernel
Solution:
  Reduced the quantum size to a level (via hit & trial) which now gives the illusion of simultaneous memory transactions (from all smp cores) received by our memory system when all apps are running concurrently

## Slide 7: Current System
SystemC Top
CPU Model
Ports
System Bus
(Rest of Platform)
0_L1_i
0_L1_d
L2
Memory
System
0_i/d
3_i/d

## Slide 8: Strategy for monitoring system performance
As OVP models are LT models so they don’t focus on detailed timing aspects of HW (to enable fast simulation)
We will use cache hits/misses within our memory system to annotate timing information that will later be used to evaluate system performance in response to standard benchmarks for various cache designs

## Slide 9: Current Status
Integrated custom memory system model (SystemC based) with the cpu
  The cache model is designed to support various configurations
    Cache block size, Num of sets, Set associativity
    Write-back/ Write-through on write hit
    Write-allocate/ Write-no-allocate on write miss
    LRU/ FIFO/ Random policies for block replacement
  For multi-level caches, strict inclusion is designed
  Sanity testing for the entire memory system model done
  Different timing annotations for cache events like hits, misses, eviction – these are observed when running simple Linux application using clock() function
A cache monitor peripheral is designed that keeps track of individual cache hits/misses via its registers. This peripheral is connected with the system bus and is readable from the Linux kernel using its memory mapped address
Looking for other VP alternatives like QEMU, GEM5 etc where we could get specifically ARMv8_A systems running and then integrate our custom models in a similar fashion