## Slide 1: Cache Partitioning Simulation Model
Uzair Sharif

## Slide 2: Outline
Objective
Virtual Platforms
Model; Design and Implementation
Performance Analysis
Conclusion

## Slide 3: Objective
Set up a full system simulation framework
  Based on ARM ISA (like ARMv8)
  Multicore CPUs
  Setup OS for workload analysis
Integrate own cache-hierarchy within the system
  Develop in SystemC for portability
Analyze Cache Pollution effects on multicore system
Cache partitioning scheme as viable solution to tackle Cache Pollution?

## Slide 4: Virtual Platform
Virtual Platforms
  Captures HW in an executable program
  Run executable to simulate system
Primarily used for
  Computer Architecture research
  Early SW development before availability of actual HW
Proprietary solutions
  ARM Fast Models, Cadence Virtual System Platform, Synopsys Platform Creator etc
Open Source solutions
  QEMU, OVP, GEM5 etc
OVP
  Open-source; C++ based; primarily used for early SW development
  Easy integration with custom SystemC modules
  License issues for ARMv8 based systems
GEM5
  Open-source, Python-C++ based; primarily used for computer architecture research
  Highly modular design incorporating high configurability
  Increasingly used in industry now e.g ARM Research

## Slide 5: Model Design
Block Size | 64 B
Partition Config. Granularity | Entire cache (1 block)
Eviction Policy | Random
Write Hit Policy | Write-back
Write Miss Policy | Write-Allocate
L1 Size | 32 KB
L1 Associativity | 2
L2 Size | 2 MB
L2 Associativity | 8
Cache specs
Block Diagram

## Slide 6: Model Implementation
Configurable Cache Hierarchy Models
  In SystemC
  Strictly inclusive property
  Configurable as per #blocks, block size, eviction policy etc
Removing gem5 cache hierarchy
  Within gem5 system, cache hierarchy directly interfaced with CPUs
  Replaced built-in cache hierarchy by stub modules that act as ports to external SystemC world
  Implemented gem5 memory semantics within the memory module
SystemC integration
  Using the patch provided by TU Kaiserslautern research team
  Modified the patch so as to directly interface with gem5 CPUs instead of gem5 system bus
Timing annotations
  Implemented timing model within SystemC cache modules based on hits/misses
  Timing annotations effect integrated into gem5
Cache Register interface
  Cache hits/misses estimation at run-time
  Modify cache partition allocation at run-time

## Slide 7: Performance Analysis
Cache benchmarking via LLCBench suite on primary core
Load application on other core interfering with benchmark application
Chart: Vector Size (kB)
| 65536 | 98304 | 131072 | 196608 | 262144 | 393216 | 524288 | 786432 | 1048576 | 1572864 | 2097152 | 3145728 | 4194304 | 6291456 | 8388608 | 12582912 | 16777216 | 25165824 | 33554432
No Partitioning (best case) | 0.03646 | 0.046402 | 0.058965 | 0.083634 | 0.10822 | 0.16506 | 0.2217 | 0.36699 | 0.51666 | 0.9916 | 2.7171 | 60.746 | 81.3328 | 94.8009 | 98.3553 | 99.7945 | 99.9509 | 99.975 | 99.972
No Partitioning (worst case) | 0.65867 | 0.95534 | 1.2753 | 1.8726 | 2.4662 | 6.1722 | 9.7209 | 21.6178 | 36.0887 | 62.1846 | 78.5188 | 92.8022 | 97.3814 | 98.1689 | 99.579 | 99.8865 | 99.9279 | 99.9444 | 99.9227
Partitioning (12 % Allocation) | 0.077083 | 0.084373 | 0.12026 | 1.3078 | 1.4434 | 67.0652 | 99.9671 | 99.9702 | 99.9703 | 99.9681 | 99.9705 | 99.9458 | 99.9603 | 99.9692 | 99.9701 | 99.9674 | 99.9722 | 99.969 | 99.97
Partitioning (25 % Allocation) | 0.034483 | 0.045468 | 0.058887 | 0.086451 | 0.1103 | 0.26422 | 0.56736 | 66.8681 | 85.7543 | 96.7442 | 99.1682 | 99.8997 | 99.9551 | 99.9654 | 99.9642 | 99.9705 | 99.9676 | 99.9693 | 99.9669
Partitioning (37 % Allocation) | 0.030699 | 0.042826 | 0.055195 | 0.081029 | 0.10494 | 0.18291 | 0.25987 | 0.76152 | 50.3662 | 83.4457 | 93.4781 | 98.7549 | 99.73 | 99.9571 | 99.9643 | 99.9696 | 99.9667 | 99.9742 | 99.9669
Partitioning (50 % Allocation) | 0.034371 | 0.046167 | 0.059041 | 0.083852 | 0.10846 | 0.17688 | 0.2482 | 0.46249 | 1.133 | 61.9343 | 82.498 | 95.3585 | 98.5831 | 99.8313 | 99.954 | 99.965 | 99.9662 | 99.9679 | 99.9669

## Slide 8: Performance Analysis
Chart: Vector Size (B)
| 256 | 384 | 512 | 768 | 1024 | 1536 | 2048 | 3072 | 4096 | 6144 | 8192 | 12288 | 16384 | 24576 | 32768
No Partitioning (best case) | 40 | 33.3333 | 34.7826 | 43.3333 | 40 | 50 | 57.1429 | 66.6667 | 67.3684 | 76.5625 | 72.2222 | 79.1165 | 73.9496 | 1.742 | 3.0061
No Partitioning (worst case) | 100 | 97.8022 | 98.3193 | 97.1098 | 97.7876 | 96.7456 | 97.3094 | 97.3254 | 97.6744 | 98.4421 | 96.5498 | 98.1355 | 97.565 | 19.374 | 29.6407
Partitioning (12 % Allocation) | 66.6667 | 81.8182 | 100 | 94.1176 | 95.2381 | 76.4706 | 83.7209 | 71.4286 | 80.9524 | 89.1304 | 83.1858 | 90.0285 | 90.101 | 5.7943 | 4.6368
Partitioning (25 % Allocation) | 45.4545 | 40 | 45 | 44.4444 | 51.6129 | 56.5217 | 64.1509 | 65.3333 | 68.4211 | 78.626 | 71.9388 | 81.1808 | 84.9351 | 4.1015 | 3.5945
Partitioning (37 % Allocation) | 33.8266 | 36.6667 | 35.793 | 49.6589 | 48.2468 | 35.0181 | 48.0744 | 45.2632 | 42.5054 | 47.3799 | 40.7439 | 45.1533 | 46.3042 | 6.0332 | 3.9456
Partitioning (50 % Allocation) | 32.8547 | 36.4793 | 50.8219 | 49.078 | 46.7697 | 45.8387 | 45.8435 | 51.2552 | 47.4576 | 37.0482 | 41.059 | 54.1978 | 38.1853 | 34.4365 | 3.9594

## Slide 9: Conclusion
Setup ARMv8 based simulation model
  Multicores running SMP OS kernel
  Custom SystemC cache hierarchy
Cache Pollution
Cache Partitioning to tackle Cache Pollution

## Slide 10
QUESTIONS??