Modeling Cache effects for ARM based platforms

---
OVP simulation environment
- Open Source tools
- Customizability
- SystemC, TLM2.0 support

---
OVP simulation environment
- Complete simulation setup for ARM platforms
- SMP-Linux kernel running on platform
- Demos provided to quickly get the system up and running

---
Our Platform setup

---
Starting out with the platform
- Need valid OVP license to build this platform
- OVP stuff is 32 bits so have to use 32 bit SystemC library
- Have to compile & link with -m32 option for gcc on 64bit host

---
Starting out with the platform
- Successfully built the simulation executable
- Running the executable boots linux-smp kernel

---
Starting out with the platform
- By default, the OVP SystemC models use SystemC DMI interface
- This makes instruction simulation very fast – linux kernel boots within seconds – but no visibility
- If DMI is disabled for visibility then it takes 35-40 mins to boot linux

---
Custom Linux Application
- OVP recommends Sourcery Codebench toolchain for ARM GNU/Linux (Open-source)
- Built a simple C HelloWorld application (.elf format) targeting ARM Cortex-A9
- Ported the executable to platform's linux init-rd filesystem using OVP utility

---
Internals of Platform model
All the sockets are using SystemC TLM interface
ARM_CA9_Mpx4
Memory
Memory bus
Peripheral bus
System bus

---
Internals of Platform model
- All SystemC models in platforms use Loosely Timed Coding style using b_transport() socket interface
- How the memory requests (instruction/data) flow from CPU to Memory model?
  - For simulation efficiency, OVP CPU models use transport_dbg() socket interface for instruction fetches first
  - Followed by actual instruction fetch via b_transport()
  - So support for transport_dbg() needed in any SystemC module to interconnect it with CPU

---
Internals of Platform model
- Only one Instruction/Data socket pair for the whole CPU
- No way to identify which SMP core actually requested the memory transaction
- To enable this capability, we customized the OVP CPU model

---
Customization of OVP CPU model
- Internally all the OVP SystemC models use ICM API
- The OVP CPU model uses icmCpuMasterPort class
  - This translates the internal memory transaction to SystemC TLM transaction and transmits via socket
  - Increased the Instruction/Data pair sockets in this class (one pair for each smp core)
  - Within this class, we figured out the actual SMP core using ICM API
  - Directed the memory transaction then to corresponding socket

---
Customization of OVP CPU model
icmCpu
Master
Port
logic
Custom SystemC
Model
ARM Cortex-A9-Mpx4
System bus
System bus
System bus
System bus

---
Starting out with cache model
- Developed a simple cache model using SystemC
- The model currently supports
  - Configurable cache size in bytes
  - Configurable cache line size in bytes
  - Set-associativity
  - Write-back/Write-through update schemes
  - LRU, LFU, random eviction policy

---
Starting out with cache model
- Only uses tags & status info for each cache block
- Timing modeled
  - Cache lookup delay
  - Cache2cpu transfer delay
  - Cpu2cache transfer delay
  - Cache2mem transfer delay
  - Mem2cache transfer delay
- No support for cache coherency yet

---
Integration in platform
- After sanity testing, we integrated the cache model within the platform
- Used in between the CPU and System Bus
- DMI is disabled on CPU so as to get memory requests onto cache model
- But in cache, DMI is enabled to increase simulation speed – linux kernel boots in ~5 minutes

---
Integration in platform
- Built a simple linux app that causes each of smp cores to issue memory transactions
- Each smp core accesses memory in its own dedicated space so as not to cause overlapping
- Cache timing delays are being observed in linux application execution time

---
Future work
- Now looking into the possibility of using shared L2 cache for the whole CPU
- Coherency support in cache model

---
Support
- Suitable documentation of source code
- Right now, maintaining a git repo for project code on github

---
Questions